PRODUCT DATA

FORMULA 2188-F

BOILER WATER ALKALINITY BUILDER

DESCRIPTION AND USE

FORMULA 2188-F is a concentrated alkalinity builder for the treatment of boiler systems supplied in liquid form.  The product concentration has been adjusted to optimize freeze protection while providing the maximum alkalinity adjustment per pound of product available.  It is recommended for use in any boiler system requiring additional alkalinity to assure proper reactions occur in the boiler water.  The product will not add additional carbon dioxide to the steam produced.

FORMULA 2188-F is specifically formulated so that the product ingredients comply with FDA regulations as published in CFR - 21 part 173.310 entitled "Boiler Water Additives".  It is USDA registered for use in boilers where steam contacts food or edible products.

CHEMICAL FEEDING AND CONTROL

FORMULA 2188-F is normally mixed in a chemical feed tank with other treatment chemicals.  Steel, stainless steel or plastic may be used in the chemical feed system.  However, copper, copper alloys and aluminum must be avoided.

FORMULA 2188-F is normally controlled by an alkalinity test on the boiler water.  Control ranges can vary widely depending upon both makeup water characteristics and system operating conditions and will be specified by the technical representative servicing the facility.

TYPICAL PROPERTIES

Appearance	Clear colorless liquid

Odor	Odorless

Specific Gravity	1.266-1.274

Flash Point	None

pH(undiluted)	14.0

Freeze Point	2oC(35oF)

SAFETY AND HANDLING

FORMULA 2188-F may be toxic by ingestion and due to its high causticity, is corrosive to mucous membranes.  Do not take internally.  If ingested, drink at least two (2) glasses of water and get medical attention. Do NOT induce vomiting.  Contact with eyes causes severe irritation or burns and possible blindness.  If eyes are contacted, immediately flush with clear water for 15 minutes and get medical attention.  For skin contact, wash with soap and water.  For additional information, see the Material Safety Data Sheet provided with this product.

PACKAGING

FORMULA 2188-F is packaged in 55, 30, and 15 gallon, non-returnable plastic drums.  Also, 6 gallon pails are available by special order.