PRODUCT DATA

FORMULA 2040-F

BOILER WATER TREATMENT

DESCRIPTION AND USE

FORMULA 2040-F is a concentrated phosphate based formulation with a multifunctional acrylic copolymer dispersant designed for use as a boiler water treatment.  The product is designed for use in boiler systems having softened makeup water and operated on the phosphate cycle.

FORMULA 2040-F incorporates one of the newest polymer dispersant technologies available for use in modern, high heat transfer boilers.  It is specifically formulated so that the product ingredients comply with FDA regulations published in CFR - 21 part 173.310 entitled "Boiler Water Additives".  It is USDA registered (application pending) for use in boilers where steam contacts food or edible products.

CHEMICAL FEEDING AND CONTROL

FORMULA 2040-F is normally fed continuously to the system being treated.  However, shot feeding may be satisfactory in some circumstances.  The product may be fed neat or diluted and mixed in a chemical feed tank with the other materials required to complete the program.  Normal materials of construction are satisfactory for the chemical feed system.  However, copper, copper alloys, and aluminum metallurgies must be avoided.

FORMULA 2040-F is controlled by a phosphate test on the boiler water.  The specific control ranges vary depending upon system operating conditions and will be specified by the technical representative servicing the facility.

TYPICAL PROPERTIES

Appearance	Clear colorless liquid

Odor	Characteristic

Flash Point	None

Specific gravity	1.105-1.113

pH(undiluted)	11.2+ 0.4

Freeze Point	<-3oC(27oF)

SAFETY AND HANDLING

FORMULA 2040-F may be toxic by ingestion.  Do not take internally.  If ingested, drink at least two (2) glasses of water and get medical attention.  Contact with eyes causes irritation or burns.  If eyes are contacted, immediately flush with clear water for 15 minutes and if irritation persists, get medical attention.  For skin contact, wash with soap and water.  For additional information, see the Material Safety Data Sheet provided with this product.

PACKAGING

FORMULA 2040-F is packaged in 55, 30, and 15 gallon, non-returnable plastic drums and 5 or 6 gallon pails.